## Slide 1
© 2015 by McGraw-Hill Education. This is proprietary material solely for authorized instructor use. Not authorized for sale or distribution in any manner. This document may not be copied, scanned, duplicated, forwarded, distributed, or posted on a website, in whole or part.
Chapter 3
Load and Stress Analysis
Lecture Slides

## Slide 2: Chapter Outline

## Slide 3: Free-Body Diagram Example 3–1

## Slide 4: Equilibrium
A system that is motionless, or has constant velocity, is in equilibrium.
The sum of all force vectors and the sum of all moment vectors acting on a system in equilibrium is zero.

## Slide 5: Free-Body Diagram Example 3–1
Fig. 3–1

## Slide 6: Free-Body Diagram Example 3–1

## Slide 7: Free-Body Diagram Example 3–1

## Slide 8: Free-Body Diagram Example 3–1

## Slide 9: Shear Force and Bending Moments in Beams
Cut beam at any location x1
Internal shear force V and bending moment M must ensure equilibrium
Fig. 3−2

## Slide 10: Sign Conventions for Bending and Shear
Fig. 3–3

## Slide 11: Distributed Load on Beam
Distributed load q(x) called load intensity
Units of force per unit length
Fig. 3–4

## Slide 12: Relationships between Load, Shear, and Bending
The change in shear force from A to B is equal to the area of the loading diagram between xA and xB.
The change in moment from A to B is equal to the area of the shear-force diagram between xA and xB.

## Slide 13: Shear-Moment Diagrams
Fig. 3–5

## Slide 14: Moment Diagrams – Two Planes
Fig. 3–24

## Slide 15: Combining Moments from Two Planes
Add moments from two planes as perpendicular vectors
Fig. 3–24

## Slide 16: Singularity Functions
A notation useful for integrating across discontinuities
Angle brackets indicate special function to determine whether forces and moments are active
Table 3–1

## Slide 17: Example 3–2
Fig. 3–5

## Slide 18: Example 3–2 (continued)
Answer
Answer
Answer

## Slide 19: Example 3–2 (continued)

## Slide 20: Example 3–3
Fig. 3–6

## Slide 21: Example 3–3 (continued)

## Slide 22: Example 3–3 (continued)
Fig. 3–6

## Slide 23: Stress
Normal stress is normal to a surface, designated by s
Tangential shear stress is tangent to a surface, designated by t
Normal stress acting outward on surface is tensile stress
Normal stress acting inward on surface is compressive stress
U.S. Customary units of stress are pounds per square inch (psi)
SI units of stress are newtons per square meter (N/m2)
1 N/m2 = 1 pascal (Pa)

## Slide 24: Stress element
Represents stress at a point
Coordinate directions are arbitrary
Choosing coordinates which result in zero shear stress will produce principal stresses

## Slide 25: Cartesian Stress Components
Defined by three mutually orthogonal surfaces at a point within a body
Each surface can have normal and shear stress
Shear stress is often resolved into perpendicular components
First subscript indicates direction of surface normal
Second subscript indicates direction of shear stress
Fig. 3−7
Fig. 3−8 (a)

## Slide 26: Cartesian Stress Components
Defined by three mutually orthogonal surfaces at a point within a body
Each surface can have normal and shear stress
Shear stress is often resolved into perpendicular components
First subscript indicates direction of surface normal
Second subscript indicates direction of shear stress

## Slide 27: Cartesian Stress Components
In most cases, “cross shears” are equal
Plane stress occurs when stresses on one surface are zero
Fig. 3−8

## Slide 28: Plane-Stress Transformation Equations
Cutting plane stress element at an arbitrary angle and balancing stresses gives plane-stress transformation equations
Fig. 3−9

## Slide 29: Principal Stresses for Plane Stress
Differentiating Eq. (3–8) with respect to f and setting equal to zero maximizes s and gives
The two values of 2fp are the principal directions.
The stresses in the principal directions are the principal stresses.
The principal direction surfaces have zero shear stresses.
Substituting Eq. (3–10) into Eq. (3–8) gives expression for the non-zero principal stresses.
Note that there is a third principal stress, equal to zero for plane stress.

## Slide 30: Extreme-value Shear Stresses for Plane Stress
Performing similar procedure with shear stress in Eq. (3–9), the maximum shear stresses are found to be on surfaces that are ±45º from the principal directions.
The two extreme-value shear stresses are

## Slide 31: Maximum Shear Stress
There are always three principal stresses. One is zero for plane stress.
There are always three extreme-value shear stresses.
The maximum shear stress is always the greatest of these three.
Eq. (3–14) will not give the maximum shear stress in cases where there are two non-zero principal stresses that are both positive or both negative.
If principal stresses are ordered so that s1 > s2 > s3, then tmax = t1/3

## Slide 32: Mohr’s Circle Diagram
A graphical method for visualizing the stress state at a point
Represents relation between x-y stresses and principal stresses
Parametric relationship between s and t (with 2f as parameter)
Relationship is a circle with center at C = (s, t) = [(s x + s y)/2, 0 ] and radius of

## Slide 33: Mohr’s Circle Diagram
Fig. 3−10

## Slide 34: Example 3–4
Fig. 3−11

## Slide 35: Example 3–4 (continued)

## Slide 36: Example 3–4 (continued)
Fig. 3−11

## Slide 37: Example 3–4 (continued)
Fig. 3−11

## Slide 38: Example 3–4 (continued)
Fig. 3−11(d)

## Slide 39: Example 3–4 (continued)

## Slide 40: Example 3–4 (continued)

## Slide 41: Example 3–4 Summary
x-y orientation
Principal stress orientation
Max shear orientation

## Slide 42: General Three-Dimensional Stress
All stress elements are actually 3-D.
Plane stress elements simply have one surface with zero stresses.
For cases where there is no stress-free surface, the principal stresses are found from the roots of the cubic equation
Fig. 3−12

## Slide 43: General Three-Dimensional Stress
Always three extreme shear values
Maximum Shear Stress is the largest
Principal stresses are usually ordered such that s1 > s2 > s3, in which case tmax = t1/3
Fig. 3−12

## Slide 44: Elastic Strain
Hooke’s law
E is Young’s modulus, or modulus of elasticity
Tension in on direction produces negative strain (contraction) in a perpendicular direction.
For axial stress in x direction,
The constant of proportionality n is Poisson’s ratio
See Table A–5 for values for common materials.

## Slide 45: Elastic Strain
For a stress element undergoing sx, sy, and sz, simultaneously,

## Slide 46: Elastic Strain
Hooke’s law for shear:
Shear strain g is the change in a right angle of a stress element when subjected to pure shear stress.
G is the shear modulus of elasticity or modulus of rigidity.
For a linear, isotropic, homogeneous material,

## Slide 47: Uniformly Distributed Stresses
Uniformly distributed stress distribution is often assumed for pure tension, pure compression, or pure shear.
For tension and compression,
For direct shear (no bending present),

## Slide 48: Normal Stresses for Beams in Bending
Straight beam in positive bending
x axis is neutral axis
xz plane is neutral plane
Neutral axis is coincident with the centroidal axis of the cross section
Fig. 3−13

## Slide 49: Normal Stresses for Beams in Bending
Bending stress varies linearly with distance from neutral axis, y
I is the second-area moment about the z axis
Fig. 3−14

## Slide 50: Normal Stresses for Beams in Bending
Maximum bending stress is where y is greatest.
c is the magnitude of the greatest y
Z = I/c is the section modulus

## Slide 51: Assumptions for Normal Bending Stress
Pure bending (though effects of axial, torsional, and shear loads are often assumed to have minimal effect on bending stress)
Material is isotropic and homogeneous
Material obeys Hooke’s law
Beam is initially straight with constant cross section
Beam has axis of symmetry in the plane of bending
Proportions are such that failure is by bending rather than crushing, wrinkling, or sidewise buckling
Plane cross sections remain plane during bending

## Slide 52: Example 3–5
Dimensions in mm
Fig. 3−15

## Slide 53: Example 3–5 (continued)

## Slide 54: Example 3–5 (continued)

## Slide 55: Example 3–5 (continued)

## Slide 56: Example 3–5 (continued)

## Slide 57: Two-Plane Bending
Consider bending in both xy and xz planes
Cross sections with one or two planes of symmetry only
For solid circular cross section, the maximum bending stress is

## Slide 58: Example 3–6
Fig. 3−16

## Slide 59: Example 3–6 (continued)
Fig. 3−16

## Slide 60: Example 3–6 (continued)
Answer
Answer

## Slide 61: Example 3–6 (continued)
Answer

## Slide 62: Shear Stresses for Beams in Bending
Fig. 3−17

## Slide 63: Transverse Shear Stress
Transverse shear stress is always accompanied with bending stress.
Fig. 3−18

## Slide 64: Transverse Shear Stress in a Rectangular Beam

## Slide 65: Maximum Values of Transverse Shear Stress
Table 3−2

## Slide 66: Significance of Transverse Shear Compared to Bending
Example: Cantilever beam, rectangular cross section
Maximum shear stress, including bending stress (My/I) and transverse shear stress (VQ/Ib),

## Slide 67: Significance of Transverse Shear Compared to Bending
Critical stress element (largest tmax) will always be either
  Due to bending, on the outer surface (y/c=1), where the transverse shear is zero
  Or due to transverse shear at the neutral axis (y/c=0), where the bending is zero
Transition happens at some critical value of L/h
Valid for any cross section that does not increase in width farther away from the neutral axis.
  Includes round and rectangular solids, but not I beams and channels

## Slide 68: Example 3–7
Fig. 3−20

## Slide 69: Example 3–7 (continued)
Fig. 3−20(b)

## Slide 70: Example 3–7 (continued)
Fig. 3−20(c)

## Slide 71: Example 3–7 (continued)

## Slide 72: Example 3–7 (continued)

## Slide 73: Example 3–7 (continued)

## Slide 74: Example 3–7 (continued)

## Slide 75: Torsion
Torque vector – a moment vector collinear with axis of a mechanical element
A bar subjected to a torque vector is said to be in torsion
Angle of twist, in radians, for a solid round bar
Fig. 3−21

## Slide 76: Torsional Shear Stress
For round bar in torsion, torsional shear stress is proportional to the radius r
Maximum torsional shear stress is at the outer surface

## Slide 77: Assumptions for Torsion Equations
Equations (3–35) to (3–37) are only applicable for the following conditions
  Pure torque
  Remote from any discontinuities or point of application of torque
  Material obeys Hooke’s law
  Adjacent cross sections originally plane and parallel remain plane and parallel
  Radial lines remain straight
    Depends on axisymmetry, so does not hold true for noncircular cross sections
Consequently, only applicable for round cross sections

## Slide 78: Torsional Shear in Rectangular Section
Shear stress does not vary linearly with radial distance for rectangular cross section
Shear stress is zero at the corners
Maximum shear stress is at the middle of the longest side
For rectangular b x c bar, where b is longest side

## Slide 79: Power, Speed, and Torque
Power equals torque times speed
A convenient conversion with speed in rpm
where H = power, W
n = angular velocity, revolutions per minute

## Slide 80: Power, Speed, and Torque
In U.S. Customary units, with unit conversion built in

## Slide 81: Example 3–8
Fig. 3−22

## Slide 82: Example 3–8 (continued)
Fig. 3−23

## Slide 83: Example 3–8 (continued)

## Slide 84: Example 3–8 (continued)

## Slide 85: Example 3–8 (continued)

## Slide 86: Example 3–8 (continued)

## Slide 87: Example 3–8 (continued)

## Slide 88: Example 3–9
Fig. 3−24

## Slide 89: Example 3–9 (continued)
Fig. 3−24

## Slide 90: Example 3–9 (continued)
Fig. 3−24

## Slide 91: Example 3–9 (continued)

## Slide 92: Example 3–9 (continued)
Fig. 3−24

## Slide 93: Example 3–9 (continued)

## Slide 94: Closed Thin-Walled Tubes
Wall thickness t << tube radius r
Product of shear stress times wall thickness is constant
Shear stress is inversely proportional to wall thickness
Total torque T is
Am is the area enclosed by the section median line
Fig. 3−25

## Slide 95: Closed Thin-Walled Tubes
Solving for shear stress
Angular twist (radians) per unit length
Lm is the length of the section median line

## Slide 96: Example 3–10
Fig. 3−26

## Slide 97: Example 3–10 (continued)

## Slide 98: Example 3–11
Solution

## Slide 99: Open Thin-Walled Sections
When the median wall line is not closed, the section is said to be an open section
Some common open thin-walled sections
Torsional shear stress
where T = Torque, L = length of median line, c = wall thickness, G = shear modulus, and q1 = angle of twist per unit length
Fig. 3−27

## Slide 100: Open Thin-Walled Sections
Shear stress is inversely proportional to c2
Angle of twist is inversely proportional to c3
For small wall thickness, stress and twist can become quite large
Example:
  Compare thin round tube with and without slit
  Ratio of wall thickness to outside diameter of 0.1
  Stress with slit is 12.3 times greater
  Twist with slit is 61.5 times greater

## Slide 101: Example 3–12

## Slide 102: Example 3–12 (continued)

## Slide 103: Example 3–12 (continued)

## Slide 104: Stress Concentration
Localized increase of stress near discontinuities
Kt is Theoretical (Geometric) Stress Concentration Factor

## Slide 105: Theoretical Stress Concentration Factor
Graphs available for standard configurations
See Appendix A–15 and A–16 for common examples
Many more in Peterson’s Stress-Concentration Factors
Note the trend for higher Kt at sharper discontinuity radius, and at greater disruption
Fig. A–15–1
Fig. A–15–9

## Slide 106: Stress Concentration for Static and Ductile Conditions
With static loads and ductile materials
  Highest stressed fibers yield (cold work)
  Load is shared with next fibers
  Cold working is localized
  Overall part does not see damage unless ultimate strength is exceeded
  Stress concentration effect is commonly ignored for static loads on ductile materials

## Slide 107: Techniques to Reduce Stress Concentration
Increase radius
Reduce disruption
Allow “dead zones” to shape flowlines more gradually

## Slide 108: Example 3–13
Fig. 3−30

## Slide 109: Example 3–13 (continued)
Fig. A−15−1

## Slide 110: Example 3–13 (continued)

## Slide 111: Example 3–13 (continued)
Fig. A−15−5

## Slide 112: Stresses in Pressurized Cylinders
Cylinder with inside radius ri, outside radius ro, internal pressure pi, and external pressure po
Tangential and radial stresses,
Fig. 3−31

## Slide 113: Stresses in Pressurized Cylinders
Special case of zero outside pressure, po = 0
Fig. 3−32

## Slide 114: Stresses in Pressurized Cylinders
If ends are closed, then longitudinal stresses also exist

## Slide 115: Thin-Walled Vessels
Cylindrical pressure vessel with wall thickness 1/10 or less of the radius
Radial stress is quite small compared to tangential stress
Average tangential stress
Maximum tangential stress
Longitudinal stress (if ends are closed)

## Slide 116: Example 3–14
Solution

## Slide 117: Example 3–14 (continued)

## Slide 118: Stresses in Rotating Rings
Rotating rings, such as flywheels, blowers, disks, etc.
Tangential and radial stresses are similar to thick-walled pressure cylinders, except caused by inertial forces
Conditions:
  Outside radius is large compared with thickness (>10:1)
  Thickness is constant
  Stresses are constant over the thickness
Stresses are

## Slide 119: Press and Shrink Fits
Two cylindrical parts are assembled with radial interference d
Pressure at interface
If both cylinders are of the same material
Fig. 3−33

## Slide 120: Press and Shrink Fits
Eq. (3–49) for pressure cylinders applies
For the inner member, po = p and pi = 0
For the outer member, po = 0 and pi = p

## Slide 121: Temperature Effects
Normal strain due to expansion from temperature change
where a is the coefficient of thermal expansion
Thermal stresses occur when members are constrained to prevent strain during temperature change
For a straight bar constrained at ends, temperature increase will create a compressive stress
Flat plate constrained at edges

## Slide 122: Coefficients of Thermal Expansion

## Slide 123: Curved Beams in Bending
In thick curved beams
  Neutral axis and centroidal axis are not coincident
  Bending stress does not vary linearly with distance from the neutral axis
Fig. 3−34

## Slide 124: Curved Beams in Bending
ro = radius of outer fiber
ri = radius of inner fiber
rn = radius of neutral axis
rc = radius of centroidal axis
h = depth of section
co= distance from neutral axis to outer fiber
ci = distance from neutral axis to inner fiber
e = rc – rn, distance from centroidal axis to neutral axis
M = bending moment; positive M decreases curvature
Fig. 3−34

## Slide 125: Curved Beams in Bending
Location of neutral axis
Stress distribution
Stress at inner and outer surfaces

## Slide 126: Example 3–15
Fig. 3−35

## Slide 127: Example 3–15 (continued)
Fig. 3−35(b)

## Slide 128: Example 3–15 (continued)
Fig. 3−35(c)

## Slide 129: Formulas for Sections of Curved Beams (Table 3–4)

## Slide 130: Formulas for Sections of Curved Beams (Table 3–4)

## Slide 131: Alternative Calculations for e
Approximation for e, valid for large curvature where e is small with rn ≈ rc
Substituting Eq. (3–66) into Eq. (3–64), with rn – y = r, gives

## Slide 132: Example 3–16
Fig. 3−36

## Slide 133: Example 3–16 (continued)

## Slide 134: Contact Stresses
Two bodies with curved surfaces pressed together
Point or line contact changes to area contact
Stresses developed are three-dimensional
Called contact stresses or Hertzian stresses
Common examples
  Wheel rolling on rail
  Mating gear teeth
  Rolling bearings

## Slide 135: Spherical Contact Stress
Two solid spheres of diameters d1 and d2 are pressed together with force F
Circular area of contact of radius a

## Slide 136: Spherical Contact Stress
Pressure distribution is hemispherical
Maximum pressure at the center of contact area
Fig. 3−36

## Slide 137: Spherical Contact Stress
Maximum stresses on the z axis
Principal stresses
From Mohr’s circle, maximum shear stress is

## Slide 138: Spherical Contact Stress
Plot of three principal stress and maximum shear stress as a function of distance below the contact surface
Note that tmax peaks below the contact surface
Fatigue failure below the surface leads to pitting and spalling
For poisson ratio of 0.30, tmax = 0.3 pmax at depth of z = 0.48a
Fig. 3−37

## Slide 139: Cylindrical Contact Stress
Two right circular cylinders with length l and diameters d1 and d2
Area of contact is a narrow rectangle of width 2b and length l
Pressure distribution is elliptical
Half-width b
Maximum pressure
Fig. 3−38

## Slide 140: Cylindrical Contact Stress
Maximum stresses on z axis

## Slide 141: Cylindrical Contact Stress
Plot of stress components and maximum shear stress as a function of distance below the contact surface
For poisson ratio of 0.30, tmax = 0.3 pmax at depth of z = 0.786b
Fig. 3−39