## Slide 1
Chapter 11
Rolling-Contact Bearings
Lecture Slides
© 2015 by McGraw-Hill Education. This is proprietary material solely for authorized instructor use. Not authorized for sale or distribution in any manner. This document may not be copied, scanned, duplicated, forwarded, distributed, or posted on a website, in whole or part.

## Slide 2: Chapter Outline

## Slide 3: Nomenclature of a Ball Bearing
Fig. 11–1

## Slide 5
The purpose of the bearing: transfer rotational external load to structure, or vise versa.
1.Rolling-contact bearing, antifriction bearing, and rolling bearing are all used to describe the class of bearing in which the main load is transferred through elements in rolling contact rather than in sliding contact.
2.Starting (static) friction of the rolling bearing is twice the running (dynamic) friction, but is still negligible in comparison with sleeve bearing
3.Load, speed and the operating viscosity of the lubricant do affect the friction characteristics of a rolling bearing.

## Slide 6
4. Mechanical designer –
a. space limitation
b. load 大小及type of load
c. life for certain speeds, load ,…
d. vibration due to balls contact with cage
Bearing designer – fatigue loading, friction, heat, corrosion resistance, kinematics problem, material properties, lubrication, machining tolerance, assembly, inspection, use, and cost.
(Bearing manufacturing process in the next page)
太大，重心太高
加一配重

## Slide 8: Types of Ball Bearings
Fig. 11–2

## Slide 9: Types of Roller Bearings
Straight Cylindrical
Spherical Roller, thrust
Tapered roller, thrust
Needle
Tapered roller
Steep-angle tapered roller
Fig. 11–3

## Slide 10: Bearing Life Definitions
Bearing Failure: Spalling or pitting of an area of 0.01 in2
Life: Number of revolutions (or hours @ given speed) required for failure.
  For one bearing
Rating Life: Life required for 10% of sample to fail.
  For a group of bearings
  Also called Minimum Life or L10 Life
Median Life: Average life required for 50% of sample to fail.
  For many groups of bearings
  Also called Average Life or Average Median Life
  Median Life is typically 4 or 5 times the L10 Life

## Slide 11: Load Rating Definitions
Catalog Load Rating, C10: Constant radial load that causes 10% of a group of bearings to fail at the bearing manufacturer’s rating life.
  Depends on type, geometry, accuracy of fabrication, and material of bearing
  Also called Basic Dynamic Load Rating, and Basic Dynamic Capacity
Basic Load Rating, C: A catalog load rating based on a rating life of 106 revolutions of the inner ring.
  The radial load that would be necessary to cause failure at such a low life is unrealistically high.
  The Basic Load Rating is a reference value, not an actual load.

## Slide 12: Load Rating Definitions
Static Load Rating, Co: Static radial load which corresponds to a permanent deformation of rolling element and race at the most heavily stressed contact of 0.0001d.
  d = diameter of roller
  Used to check for permanent deformation
  Used in combining radial and thrust loads into an equivalent radial load
Equivalent Radial Load, Fe: Constant stationary load applied to bearing with rotating inner ring which gives the same life as actual load and rotation conditions.

## Slide 13: Load-Life Relationship
Using a regression equation to represent the line,
  a = 3 for ball bearings
  a = 10/3 for roller bearings (cylindrical and tapered roller)
Nominally identical groups of bearings are tested to the life-failure criterion at different loads.
A plot of load vs. life on log-log scale is approximately linear.
Fig. 11–4

## Slide 14: Load-Life Relationship
Applying Eq. (11–1) to two load-life conditions,
Denoting condition 1 with R for catalog rating conditions, and condition 2 with D for the desired design conditions,
The units of L are revolutions. If life is given in hours at a given speed n in rev/min, applying a conversion of 60 min/h,
Solving Eq. (a) for FR, which is just another notation for the catalog load rating,

## Slide 15: Load-Life Relationship
The desired design load FD and life LD come from the problem statement.
The rated life LR will be stated by the specific bearing manufacturer. Many catalogs rate at LR = 106 revolutions.
The catalog load rating C10 is used to find a suitable bearing in the catalog.

## Slide 16: Load-Life Relationship
It is often convenient to define a dimensionless multiple of rating life

## Slide 17: Example 11–1

## Slide 18: Reliability vs. Life
If the reliability is not 90%, sometime larger than 90%, then we need to use Eq. 11-6 or 11-7 to find the C10 at required RD , LD and FD.
At constant load, the life measure distribution is right skewed.
The Weibull distribution is a good candidate.
Defining the life measure in dimensionless form as x = L/L10, the reliability is expressed with a Weibull distribution as

## Slide 19: Reliability vs. Life
From Eq. (1–8), R = 1 – p, where p is the probability of a value of x occurring between –∞ and x.
p is the integral of the probability distribution f(x).
From the derivative of Eq. (11–4), the Weibull probability density function is

## Slide 20: Reliability vs. Life
The mean and standard deviation of f(x) are
G is the gamma function, and is tabulated in Table A–34

## Slide 21: Reliability vs. Life
Solving Eq. (11–4) for x yields

## Slide 22: Example 11–2

## Slide 23: Example 11–2 (continued)

## Slide 24: Relating Load, Life, and Reliability
Catalog information is at point A, at coordinates C10 and x10=L10/L10=1, on the 0.90 reliability contour.
The design information is at point D, at coordinates FD and xD, on the R=RD reliability contour.
The designer must move from point D to point A via point B.
Fig. 11–5

## Slide 25: Relating Load, Life, and Reliability
Along a constant reliability contour (BD), Eq. (11–2) applies:
Fig. 11–5

## Slide 26: Relating Load, Life, and Reliability
Along a constant load line (AB), Eq. (11–4) applies:
Solving for xB,
Fig. 11–5

## Slide 27: Relating Load, Life, and Reliability
Substituting xB into Eq. (a),
Noting that FB = C10, and including an application factor af,
Note that when RD = 0.90, the denominator equals one and the equation reduces to Eq. (11–3).

## Slide 28: Weibull Parameters
The Weibull parameters x0, q, and b are usually provided by the catalog.
Typical values of Weibull parameters are given on p. 601 at the beginning of the end-of-chapter problems, and shown below.
Manufacturer 1 parameters are common for tapered roller bearings
Manufacturer 2 parameters are common for ball and straight roller bearings

## Slide 29: Relating Load, Life, and Reliability
Eq. (11–9) can be simplified slightly for calculator entry. Note that
  where pf is the probability for failure
Thus Eq. (11–9) can be approximated by

## Slide 30: Example 11–3

## Slide 31: Combined Reliability of Multiple Bearings
If the combined reliability of multiple bearings on a shaft, or in a gearbox, is desired, then the total reliability is equal to the product of the individual reliabilities.
For two bearings on a shaft, R = RARB
If the bearings are to be identical, each bearing should have a reliability equal to the square root of the total desired reliability.
If the bearings are not identical, their reliabilities need not be identical, so long as the total reliability is realized.

## Slide 32: Dimension-Series Code
ABMA standardized dimension-series code represents the relative size of the boundary dimensions of the bearing cross section for metric bearings.
Two digit series number
First digit designates the width series
Second digit designates the diameter series
Specific dimensions are tabulated in catalogs under a specific series
Fig. 11–7

## Slide 33: Representative Catalog Data for Ball Bearings (Table 11–2)

## Slide 34: Representative Catalog Data for Cylindrical Roller Bearings (Table 11–3)

## Slide 35: Combined Radial and Thrust Loading
When ball bearings carry both an axial thrust load Fa and a radial load Fr, an equivalent radial load Fe that does the same damage is used.
A plot of Fe/(VFr) vs. Fa /(VFr) is obtained experimentally.
V is a rotation factor to account for the difference in ball rotations for outer ring rotation vs. inner ring roation.
  V = 1 for inner ring rotation
  V = 1.2 for outer ring rotation
Fig. 11–6

## Slide 36: Combined Radial and Thrust Loading
The data can be approximated by two straight lines
X is the ordinate intercept and Y is the slope
Basically indicates that Fe equals Fr for smaller ratios of Fa/Fr, then begins to rise when Fa/Fr exceeds some amount e
Fig. 11–6

## Slide 37: Combined Radial and Thrust Loading
It is common to express the two equations as a single equation
where
i = 1 when Fa /(VFr) ≤ e
i = 2 when Fa /(VFr) > e
X and Y factors depend on geometry and construction of the specific bearing.
Fig. 11–6

## Slide 38: Equivalent Radial Load Factors for Ball Bearings
X and Y for specific bearing obtained from bearing catalog.
Table 11–1 gives representative values in a manner common to many catalogs.
Table 11–1

## Slide 39: Equivalent Radial Load Factors for Ball Bearings
X and Y are functions of e, which is a function of Fa/C0.
C0 is the basic static load rating, which is tabulated in the catalog.
Table 11–1

## Slide 40: Bearing Life Recommendations (Table 11–4)

## Slide 41: Recommended Load Application Factors (Table 11–5)

## Slide 42: Example 11–4

## Slide 43: Example 11–4 (continued)

## Slide 44: Variable Loading

## Slide 45: Variable Loading with Piecewise Constant Loading

## Slide 46: Variable Loading with Piecewise Constant Loading

## Slide 47: Example 11–5

## Slide 48: Example 11–5 (continued)

## Slide 49: Variable Loading with Piecewise Constant Loading

## Slide 50: Variable Loading with Periodic Variation
Fig. 11–11

## Slide 51: Example 11–6

## Slide 52: Example 11–6 (continued)

## Slide 53: Example 11–7
Fig. 11–12

## Slide 54: Example 11–7

## Slide 55: Example 11–7

## Slide 56: Example 11–7

## Slide 57: Example 11–7 (continued)

## Slide 58: Tapered Roller Bearings
Straight roller bearings can carry large radial loads, but no axial load.
Ball bearings can carry moderate radial loads, and small axial loads.
Tapered roller bearings rely on roller tipped at an angle to allow them to carry large radial and large axial loads.
Tapered roller bearings were popularized by the Timken Company.

## Slide 59: Tapered Roller Bearings
Two separable parts
  Cone assembly
    Cone (inner ring)
    Rollers
    Cage
  Cup (outer ring)
Rollers are tapered so virtual apex is on shaft centerline
Taper allows for pure rolling of angled rollers
Distance a locates the effective axial location for force analysis
Fig. 11–13

## Slide 60: Mounting Directions of Tapered Roller Bearings
Mount pairs in opposite directions to counter the axial loads
Can be mounted in direct mounting or indirect mounting configurations
For the same effective spread ae, direct mounting requires greater geometric spread ag
For the same geometric spread ag, direct mounting provides smaller effect spread ae
Fig. 11–14

## Slide 61: Typical Catalog Data (Fig. 11–15)

## Slide 62: Typical Catalog Data (Fig. 11–15)

## Slide 63: Typical Catalog Data (Fig. 11–15 continued)

## Slide 64: Typical Catalog Data (Fig. 11–15 continued)

## Slide 65: Induced Thrust Load
A radial load induces a thrust reaction due to the roller angle.
K is ratio of radial load rating to thrust load rating
K is dependent on specific bearing, and is tabulated in catalog
Fig. 11–16

## Slide 66: Equivalent Radial Load
The equivalent radial load for tapered roller bearings is found in similar form as before,
Timken recommends X = 0.4 and Y = K
Fa is the net axial load carried by the bearing, including induced thrust load from the other bearing and the external axial load carried by the bearing.
Only one of the bearings will carry the external axial load

## Slide 67: Determining Which Bearing Carries External Axial Load
Regardless of mounting direction or shaft orientation, visually inspect to determine which bearing is being “squeezed”
Label this bearing as Bearing A
Fig. 11–17

## Slide 68: Net Axial Load
Generally, Bearing A (the squeezed bearing) carries the net axial load
Occasionally the induced thrust from Bearing A, FiA, is greater than the combination of the induced thrust from Bearing B, FiB, and the external axial load Fae , that is
If this happens, then Bearing B actually carries the net axial load

## Slide 69: Equivalent Radial Load
Timken recommends using the full radial load for the bearing that is not carrying the net axial load.
Equivalent radial load equation:
If the equivalent radial load is less than the original radial load, then use the original radial load.

## Slide 70: Example 11–8
Fig. 11–18

## Slide 71: Example 11–8 (continued)
Fig. 11–18

## Slide 72: Example 11–8 (continued)

## Slide 73: Example 11–8 (continued)

## Slide 74: Example 11–8 (continued)

## Slide 75: Example 11–8 (continued)

## Slide 76: Example 11–8 (continued)

## Slide 77: Realized Bearing Reliability
Eq. (11–9) was previously derived to determine a suitable catalog rated load for a given design situation and reliability goal.
An actual bearing is selected from a catalog with a rating greater than C10.
Sometimes it is desirable to determine the realized reliability from the actual bearing (that was slightly higher capacity than needed).
Solving Eq. (11–9) for the reliability,

## Slide 78: Realized Bearing Reliability
Similarly for the alternate approximate equation, Eq. (11–10),

## Slide 79: Example 11–9

## Slide 80: Realized Reliability for Tapered Roller Bearings
Substituting typical Weibull parameters for tapered roller bearings into Eqs. (11–21) and (11–22) give realized reliability equations customized for tapered roller bearings.

## Slide 81: Example 11–10

## Slide 82: Example 11–10 (continued)

## Slide 83: Example 11–11
Fig. 11–19

## Slide 84: Example 11–11 (continued)

## Slide 85: Example 11–11 (continued)

## Slide 86: Example 11–11 (continued)

## Slide 87: Bearing Lubrication
The purposes of bearing lubrication
  To provide a film of lubricant between the sliding and rolling surfaces
  To help distribute and dissipate heat
  To prevent corrosion of the bearing surfaces
  To protect the parts from the entrance of foreign matter

## Slide 88: Bearing Lubrication
Either oil or grease may be used, with each having advantages in certain situations.

## Slide 89: Some Common Bearing Mounting Configurations
Fig. 11–20
Fig. 11–21

## Slide 90: Some Common Bearing Mounting Configurations
Fig. 11–22

## Slide 91: Some Common Bearing Mounting Configurations
Fig. 11–23

## Slide 93: Duplexing
When maximum stiffness and resistance to shaft misalignment is desired, pairs of angular-contact bearings can be used in an arrangement called duplexing.
Duplex bearings have rings ground with an offset.
When pairs are clamped together, a preload is established.

## Slide 94: Duplexing Arrangements
Three common duplexing arrangements:
  DF mounting – Face to face, good for radial and thrust loads from either direction
  DB mounting – Back to back, same as DF, but with greater alignment stiffness
  DT mounting – Tandem, good for thrust only in one direction
Fig. 11–24

## Slide 95: Preferred Fits
Rotating ring usually requires a press fit
Stationary ring usually best with a push fit
Allows stationary ring to creep, bringing new portions into the load-bearing zone to equalize wear

## Slide 96: Preloading
Object of preloading
  Remove internal clearance
  Increase fatigue life
  Decrease shaft slope at bearing
Fig. 11–25

## Slide 97: Alignment
Catalogs will specify alignment requirements for specific bearings
Typical maximum ranges for shaft slopes at bearing locations

## Slide 98: Enclosures
Common shaft seals to exclude dirt and retain lubricant
Fig. 11–26